## Slide 1
Network Layer
The transport layer is responsible for establishing connections between processes on hosts, and the network layer is responsible for transmitting data from one host to another.
PDUs transmitted at the network layer are called packets.
Functions of the network layer:
Provides logical addresses for network devices.
Routes and forwards data packets.
Common network layer protocols include IPv4, IPv6, ICMP, and IGMP
Standard TCP/IP model
OSI model
Equivalent TCP/IP model
OSI MAPING
NETWORK LAYER

## Slide 2
DATA ENCAPSULATION AT THE SENDER

## Slide 3
The network layer header of a packet sent by a source device carries the network layer addresses of the source and destination devices.
Each network device (such as a router) that has the routing function maintains a routing table (like a map of the network device).
After receiving a packet, the network device reads the network layer destination address of the packet, searches the routing table for the matching entry of the destination address, and forwards the packet according to the instruction of the matching entry.
Source Ip 192.168.0.2
Destination IP 122.3.3.1